## Slide 1: Overview
Introduction to basic computer architecture concepts.
Quantitative techniques in computer design and performance evaluation.
Instruction Set Architectures (ISA): CISC, RISC, and DSP.
Processor organization and architectural overview.
Design of RISC processor: datapath and control.
Multicycle processor implementation.

## Slide 2: Basic Computer Architecture
Computer architecture defines the functional behavior of a computer system.
Focuses on CPU design, memory hierarchy, input/output systems, and interconnections.
Key components: Arithmetic Logic Unit (ALU), Control Unit, Registers, Cache, Main Memory.
Architecture impacts performance, power consumption, and cost.

## Slide 3: Von Neumann vs Harvard Architecture
Von Neumann uses a single memory for instructions and data.
Harvard architecture separates instruction and data memory.
Harvard provides higher throughput due to parallel access.
Von Neumann suffers from the bottleneck problem.

## Slide 4: Performance Metrics
Execution Time = Instruction Count × CPI × Clock Cycle Time.
Throughput measures number of tasks completed per unit time.
Latency measures delay between input and output.
Clock frequency influences processing speed.

## Slide 5: Quantitative Techniques in Computer Design
Amdahl’s Law evaluates system speedup with enhancements.
Benchmarking compares processor performance.
CPU performance equation guides architectural optimizations.
Parallelism improves computational efficiency.

## Slide 6: Measuring and Reporting Performance
Use standardized benchmarks like SPEC.
Report metrics such as MIPS, FLOPS, and IPC.
Avoid misleading averages; prefer geometric mean.
Consider power-performance tradeoffs.

## Slide 7: Instruction Set Architecture (ISA)
ISA defines interface between hardware and software.
Includes instruction formats, addressing modes, registers, and data types.
Acts as a contract for compiler and processor designers.

## Slide 8: CISC Architecture
Complex Instruction Set Computer uses large instruction sets.
Supports multi-step operations in single instruction.
Reduces program size but increases hardware complexity.
Examples: Intel x86.

## Slide 9: RISC Architecture
Reduced Instruction Set Computer uses simple instructions.
Load/store architecture separates memory and ALU operations.
Enables deep pipelining and higher clock speeds.
Examples: ARM, MIPS.

## Slide 10: DSP Processors
Optimized for signal processing applications.
Support fast multiply-accumulate operations.
Use specialized addressing modes such as circular buffering.
Widely used in audio, video, and communication systems.

## Slide 11: CISC vs RISC vs DSP
CISC: fewer instructions per program but complex decoding.
RISC: more instructions but simpler execution.
DSP: designed for real-time numeric computation.
Choice depends on application requirements.

## Slide 12: Processor Organization
Datapath handles data movement and processing.
Control unit generates signals to coordinate operations.
Registers provide fast temporary storage.
Buses enable communication between components.

## Slide 13: Datapath Components
Program Counter (PC) tracks instruction address.
Register File stores operands.
ALU performs arithmetic and logical operations.
Multiplexers route data based on control signals.

## Slide 14: Control Unit Design
Hardwired control uses combinational logic.
Microprogrammed control uses control memory.
Control signals determine datapath behavior.
Tradeoff between speed and flexibility.

## Slide 15: Single-Cycle vs Multi-Cycle
Single-cycle executes instruction in one clock cycle.
Requires long clock period.
Multi-cycle divides execution into stages.
Improves clock efficiency and resource utilization.

## Slide 16: Building a RISC Datapath
Identify instruction formats.
Determine required hardware resources.
Connect ALU, registers, memory, and PC.
Optimize for common instruction paths.

## Slide 17: RISC Control Signals
RegWrite enables register updates.
MemRead and MemWrite control memory access.
ALUSrc selects operand source.
Branch determines control flow.

## Slide 18: Multicycle Implementation Steps
Instruction Fetch.
Instruction Decode and Register Fetch.
Execution or Address Calculation.
Memory Access.
Write Back.

## Slide 19: Advantages of Multicycle Design
Shorter clock cycle than single-cycle.
Hardware reuse reduces cost.
Flexible timing for different instructions.
Better overall efficiency.

## Slide 20: Pipeline Introduction (Optional Extension)
Pipeline overlaps instruction execution.
Improves throughput significantly.
Hazards include structural, data, and control.
Requires forwarding and stall mechanisms.

## Slide 21: Modern Trends in Processor Design
Multi-core architectures dominate computing.
Energy-efficient designs are critical.
AI accelerators and GPUs complement CPUs.
Heterogeneous computing is becoming standard.

## Slide 22: Summary
Computer architecture directly impacts system performance.
Quantitative analysis guides better design choices.
RISC dominates modern embedded and mobile systems.
Multicycle datapath improves efficiency.